Ocean SoundLab
documentation version 2.0

# Overview
### Architecture

Control Data
Audio Data B
Audio Data A
Synthesizer
Audioserver
Sndlab GUI
Composer

main.synth

Pulse audio

Files

read
read
write

write
read/write

# Synthesizer
The synthesizer process executes the control data. The execution may impact the processing of waveforms and data I/O in conjunction with memory arrays and files.
The synthesizer generates audio data, that is processed by the audio server.
# AudioServer
The AudioServer process is the device driver for audio data, that is generated by the synthesizer process. It writes this data directly to the RtAudio API (github). The API is configured to work together with the UNIX Pulseaudio facility.
The properties of the AudioServer are fixed to a sampling rate of 48000 and to 16-bit of stereo output.
# SndlabGUI
The SndlabGUI was developed in parallel to the synthesizer after having a working AudioServer.
But after the Composer is available the SndlabGUI is preferably used to check out sounds and store them into instrument files as well as note sentence fragments. It is also usable to extend the standard waveforms by a spectrum . The spectrum is related to an instrument, so that specific characteristics are possible.
During the composer run the GUI functionality is switched into an observer mode.
The GUI surface uses the same nouns as the composer. For more details refer to the composer. The impact of special functions is also visible on the screen.
# comstack
the comstack is a text based editor for the interface data like a debugging tool.
# Composer
Lets say, the composer is processing a complex preset, a program. The composer compiles the program by interpreting it and generating a time ordered sequence of changes of the control data, that is executed in real time by the synthesizer, accordingly.
The composer run can be separated into phases: preprocessing -> compilation -> execution
The program line is structured as follows:
- Keyword followed by one or more words, describing the keyword specific action,
- user defined identifier name followed be an equal sign (=) followed be a value (macro definition),
- user defined notes filename, followed by a filename followed be a plus sign (+) followed by a filename (search path for notes),
- user defined :subroutine name , the subroutine name must start with a colon (:) .
- hash sign (#) followed by a user defined comment text. This text is ignored during the preprocessing phase.
### Programming/ main.synth
exit	program line at witch the processing of main.synth ends
call :subroutine	jump to a subroutine. The colon(:) marques a subroutine as such
:subroutine	the jump destination of a call
return	return the program execution one line below the previous call
include file	replace the program line where the include statement occurred by the content of file.inc . The action is performed as part of the preprocessing
variable=value	intended to make the program more readable. / Variable behaves like a macro that is applied to the complete program text, so that each occurrence of variable is replaces by value, regardless of a syntax check. The action is performed as part of the preprocessing
file=filea + fileb	append filea.kbd with the content of fileb.kbd and store it as Synthesizer/var/auto/file.kbd, where file, filea and fileb are arbitrary names without separator characters (space, tab). The search for filea and fileb is Synthesizer/etc/Notes and Synthesizer/var/auto. / The action + is performed during the interpreter run.
text "text"	print out all after keyword text

Notes:
In the last phase of the composer call the data is transformed by the Synthesizer and AudioServer into physical sound.
Special note on include files:
The location where include files should be inserted into a program file depends on the content of the include file. If it contains subroutines it must be added at the end of the main.synth program file. In all other cases it can be placed as needed and it can be included multiple times. include files may also contain include files.
Example: manage program flow with main.synth
call :syntaxtest1
call :maintest
exit
:syntaxtest1
text syntax check program flow
include lib
return

:maintest
text entering main test
pause key

The composer reports line nr and filename of a command line.
Table 1: Keywords and special characters
Keyword	short description
add	store the instrument playing notes into a memory array
adsr	Control single elements of the ADSR facility
call	Control the program flow
include	Control the program flow
instrument	assign the current instrument
notes	assign and define notes for processing
osc	Control the oscillators (Main, VCO and FMO)
play	Managing the output of memory arrays
pause	wait for some seconds before the next statement is processed
random	generate notes according to the specified rules
rec	Control the recording to the memory bank
record	Control the recording of the output
return	Control the flow of the synthesizer program
set	specify certain properties
start/stop	start/stop sub processes (Synthesizer /AudioServer)
=	defines a macro name
+	add two note files

space, tab	separator characters
"parameter text"	spaces and tab within hyphens (") are not considered to be parameter separator

# text	comment text

Remark: all internal defined keywords are compared to lower case versions, so that; add, Add, ADD are equivalent while user defined words are used as they are defined, so that: call :subroutine has a different meaning than call :Subroutine.
### add/ Play notes using an instrument
add instrument notes memory

add	short description
instrument	name of the instrument. Instrument files are generated by the SndlabGUI and stored in directory Synthesizer/etc/Instruments
notes	name of the notes file. Note files can be generated (see random) or created/edited by the SndlabGUI. In addition to that note files can be concatenated, (see programming )
memory	a memory identifier where the sound shall be stored (0..5)

Remark: the storage duration depends on the duration of notes to play.
Example: Store the sound of the instrument drums2 with notes drums3 into storage location 1 in background mode. See alo full example.

Storage1 = 1
add	drums2 drums3 Storage1
play Storage1 amp 100

text add/ Play notes using an instrument
pause key

This is the same as saying (foreground mode):

instrument load drums2	# load files drums2.kdb and drums2.spec
notes load drums3	# load file drums3.kbd
notes play on 100	# switch to notes mode
rec store 1	# store to memory 1
pause auto	# wait for sentence duration seconds
rec stop 1	# stop record on memory 1
notes play off	# switch off note playing
play 1 amp 100	# switch on memory 1 playing

text This is the same as saying (foreground mode):
pause key

The notes are repeated as long as one of the following occurs
- the Composer terminates (see pause on how to delay the composer execution)
- the storage is over written.
### ADSR
add effects to the output of the main osc.
adsr [pmw # | hall # | attack # | decay # | softfreq # | beat #]

adsr	short description
attack	control the volume of the main output from 0 to max during a beat. The attack curve is linear.
beat	0 : attack/decay is not applied 1: duration is 1 second one beat per second 2: duration is 500ms, 3 - > 250ms, 4 ->125ms
hall	add the current main osc output with phase shift
pmw	controls the width of the wave form PMW of the vco only.
decay	controls the volume of the main output from max to 0 during a beat. The decay curve is exponential.

Example:

StA2 = 2
osc main unmute
set main freq 220
set vco amp 50
adsr beat 4
adsr attack 10
adsr decay 90
adsr softfreq 0
rec store StA2
pause 5
osc main mute
rec amp StA2 100

text some osc and adsr commands
pause key

### call / return subroutine
call :subroutine

call	short description
:subroutine	the subroutine noun must start with a colon (:) as well as the subroutine section
:subroutine / ... list of composer commands ... / return	subroutine section must end with the return statement

Note: subroutine names consider lower and upper case characters.
### exit
terminates the composer execution.
### Instrument
an instrument consists of two files, name.kbd and name.spec.
instrument load filename

instrument	short description
load filename	load filename, / remark: the filename must be given without the extension .kbd

Example: load instrument file Saxophone.kbd and associated spectrum file Saxophone.spec

instrument load Saxophone
### Notes
AaBCcDdEFfGg	12 Note names representing the note values 0,1,2, ... 11 in a chromatic scale denoted as "eng". is the default notation
0123456789AB	alternative notes notation denoted as "num"
ABCDEFG	alternative notes notation. This is implicitly choose if notes set prefix is used to define the number of flats and sharps.
, (comma)	decrease the note value by one octave Example f,
' (hyphen)	increase the note value by one octave Example f'
- (minus)	increase the duration of a note by a note length Example f-
. (dot)	no note. Silence for one note length
a>b	denotes a gliding note. e.g. B-->F : Increases continuously the frequency from B to F during the note length of B (3 x min_duration). The gliding note counts as one note. Change octave from 2 to 3 by: |2B--->|3F
|# (pipe number)	set the octave for all subsequent notes to # Example |3c provides a frequency of 55 * 2³ * 2^(4/12) Hz. #=1...max_octave (see Glossary)
( note names )	polyphone notes Example (AC) generate sound of A and C in parallel. / More than two notes in parallel may result in over sampling.

notes [	load filename|
set prefix #1 #2
set octave #3
set [num] sentence rhythm |
play [ on #| off ] |
per_second # ]

notes	short description
load filename	read notes file filename
set [num] sentence rhythm	store sentence and rhythm into file tmp.kbd and load file / the optional keyword "num" allows to change to the numeric notation of notes in the note sentence.
set octave #3	set the octave for notes to value #3
set prefix #1 #2	Change to alphabet notes ABCDEFG with #1 flats (b) and #2 sharps (#) acting on file var/auto/tmp.kbd .
play [ on #4 | off ]	start / stop playing notes from real time generated sound. / #4 denotes the volume (0..100)% in case of on
per_second #5	set the #5 (1,2,4,8) of notes per seconds. This maps to a duration per note of (1000, 500, 250, 125) [msec] / The duration must be set before notes are generated. This is valid until a different value is set.

Note: after storage into StA by rec or add or + the temporary file tmp.kbd can be reused for other.
Example:
osc main mute
notes play on 100
notes per_second 2
notes set (AC).AC.DC.(DC)... 8
pause key

Example:
osc main mute
notes set "ABCD EFGF EDCB .---" 8
notes set prefix 1 0
notes play on 100
pause key

### Oscillator/osc
There are three oscillators, working together. The MAIN oscillator provides the main properties of the sound in terms of frequency, waveform, amplitude and effects (see adsr collection).
The VCO controls the volume of the main oscillator and the FMO the frequency. Both are doing this by applying their own properties in terms of frequency, waveform and volume.
Set the oscillator wave form, frequency and amplitude for a given duration
osc [main|vco|fmo] set wave_str frequency amplitude pause
osc main loop [ amp #| freq #]
osc main [mute|unmute|reset]

Table 2: Standard Waveforms
waveid	Waveform String / ( wave_str)	Wave form description
0	sine	Sine with default spectrum
1	Sine	Sine
2	SgnSin	Signed sine
3	rectangle	Rectangle
4	sawtooth	Sawtooth left
5	Sawtooth	Sawtooth right
6	triangle	Triangle
7	PMW	Pulse Wide modulation
8	random	Random Noise

The frequency should be in the range of 0 up to max_frequency [Hz] (see Glossary). Considering a sampling rate of 48000 this mean, that a wave length is separated into 13 or 14 step values. This is not so much, to describe a standard waveform or a complex one.
The amplitude is given in % of the total available amount ( 0 … 100)%.
The duration to hold the setting is given in seconds (0 … 30), depending on the memory size.
Example: To change the frequency of the VCO to the value of 500[Hz] for 5 seconds using waveform Signed Sign (2) the entry
osc vco set sgnSin 500 80 auto

One can set single aspects of the main oscillator by applying
osc [main|fmo|vco] set [wf|freq|amp] value [duration]
See also keyword set for the same .
set vco wf Sine
set vco freq 500
set vco amp 80

will do this. See also set
Another example
osc main reset
osc main set sgnSin 200 100 auto
osc main wf rectangle
osc main loop freq 400 500
pause key

### play
### Pause
Set the timer (#) or event (auto, key)
pause [#|auto|key]

pause	short description
#	A number less than 30 to wait for this number of seconds until the next composer command is executed.
auto	wait for the number of seconds the note sentence needs to play
key	wait until the <return> key is pressed

Example:
pause 10 # Wait for 10 seconds, then continue.
pause key # wait for <return> key

### random /generate notes
#### Field specification
random constant rhythm variable sentence name
Table 3: Generating Notes
random	short description
constant	a list of note values used to specify the constant part of a note sentence. / In addition the note literal "r" will be transform into a single random note
rhythm	Specifies the volume of a single note. The volume is define by the number 0,1,2,..9 and maps to a volume of 0%, 10%, 20%, ... 90%. The default volume of a note is 80%. / Ex: the rhythm 7 means each note becomes a volume of 70%, / then rhythm 69 means the volume cycle 60%90%60%90%60%90%... in the note sentence. / Ex: notes are cccc, rhythm = 0999 is the same as note= .ccc rhythm = 9
variable	A set of note names and note specifiers out of which random notes are generated. / Remark: The more often one literal occurs in the list, the more likely it is this literal is chosen. / Valid characters are: CcDdEFfGgAaH!,.-'
	, / ' / .	insert a decrese/increase/pause mark into the random word
	!c	make c mandatory in each random note word
sentence	a sequence of note words that can be a constant, variable or pause. These are denoted as c r and - . c can consist of more than one word. r is always one word. / In addition one can duplicate a sentence and switch a single word within it. see example
	sentence characters	short description
	c	replace "c" by the constant part
	r	insert a random word
	-	insert a pause word consisting of: .---
	cR	insert the reverse constant
	#	set the octave to # for the previous word. / # at the begin of the sentence will set the octave for the complete sentence
name	The generated note sentence including rhythm line is store under the user specified name name.kbd in the directory Synthesizer/var/auto

Example:
osc main mute
CONSTANT	= |2(ACD)-(ACE)-(BDF)-(BDG).
RYTHM	= 9789
VARIABLE	= (AC'D)(AC'E)(BD'F)(BD'G)G
SENTENCE	= crr-:S12
FILENAME	= lead
INSTR.	= piano
STORAGE	= 2

Random CONSTANT RYTHM VARIABLE SENTENCE FILENAME
Add INSTR. FILENAME STORAGE auto
play STORAGE amp 100
pause key

constant part c = |2(AC)r(DE)G|3(AC)c(DC).
variable note words denoted as "r" in the sentence crr- are generated out of the list c-fgCDA.'',,
The note sentence crr- is again duplicated by swapping word 1 and 2.
The resulting note sentence crr-rcr- is stored in the file Synthesizer/var/auto/lead.kbd
Remark: The sections are separated by spaces or tabs. That means that a space within a section may result in a meaningless interpretation of the command.
### rec / store sound
There are 8 storage arrays (StA)
StA Id	short description	max duration
0...5	User defined	30 sec
6	temp storage of notes sound	1 sec
7	wav-file storage	180 sec

Note: The max duration is limited by the reserved storage size.
The following commands manage the content of the StA 0...6
rec [ notes #1 | store #1| amp #1 #2| stop #1| play free]
| mute #1| clear #1 ]
rec	keyword
#1	StA id 0...5
#2	volume 0...100
store #1	store the current output of free and notes to StA #1
amp #1 #2	replay sound of StA #1 with volume #2
stop #1	stop recording on StA #1
notes #1	translate note sentence in background, generate sound, store sound in StA #1 (all in one command).
play free	switch off synchronized notes mode. The AudioServer will process what is ready for it.
mute #1	mute StA #1
clear #1	delete the content of StA #1

Example base scenario see add command (background mode) or, what you do that you hear as follows.
osc main mute	otherwise you will store one sec. osc main sound, one second note sound and so forth. See note below.
instrument load drums	load an instrument
notes load rhythm	load some notes
notes play on 100	play notes with volume 100%
rec store 1	store sound to storage array #1
pause auto	wait for some seconds (note sentence duration)
rec stop 1	stop recording on storage array #1
notes play off	switch note generating off
rec amp 1 100	play storage array #1 with volume 100%
pause key	as long as wanted

Note on storage: The storage is additive until cleared, so that one can append tracks to one StA.
### Record / to file
record current sound track to a wav and an mp3 file
record | file #1 | stop #2 | play #2 #1 | loop amp #3 ]

record	short description
file #1	record current sound track #1 seconds < 180 to StA 7
stop #2	store content of StA7 to files / var/wav/synthesizer#2.wav and var/wav/synthesizer.mp3
play #2 #1	add sound of file var/wav/synthesizer#2.wav #1 seconds to current sound.
loop amp #3

Example:
RECFILE = 77
record file 10
stop RECFILE
play RECFILE 5
text record file synthesizer77.wav
pause key

### Return / from subroutine
keyword return, see keyword call
### Set
set [octave+ | octave- | main | vco | fmo]

set	short description
octave+	increases the base_octave by one eg. from 55Hz to 110Hz
octave-	decreases the base_octave by one, but not to zero. eg. from 110Hz to 55Hz
main property #	set the property [freq|wf|amp] of oscillator main to value #
vco property #	set the property [freq|wf|amp] of oscillator vco to value #
fmo property #	set the property [freq|wf|amp] of oscillator fmo to value #

Example
set main freq 120
set the frequency of the main oscillator to 120 Hz.
### start
start server shmkey delay
start	short description
server	AudioServer|Synthesizer
shmkey	shared memory key must be identical for both servers. The value range is system dependent
delay	wait until next process step, to manage potential synchronization issues. / delay takes default "key" see pause

Example:
call :startserver

lib.inc
:startserver
start	AudioServer 10000 0
start	Synthesizer 10000 3
return

### stop
stop composer subprocesses.

# Appendix
### Directory structure
Synthesizer/bin	Executable
Synthesizer/doc	Documentation
Synthesizer/etc	Configuration
Synthesizer/etc/Instruments	Instrument files and instrument search path
Synthesizer/etc/include	main.synth and include search path
Synthesizer/etc/Notes	Note files and note search path
Synthesizer/lib	check point shared memory dump location
Synthesizer/tmp	audio raw file dump location
Synthesizer/var	variable synthesizer data
Synthesizer/var/auto	random notes and notes search path
Synthesizer/var/log	Synthesizer cumulated log
Synthesizer/var/wav	mp3 and wav files and external input files search directory

### Full Example
play two instrument with randomly generated notes
# switch off main oscillator (notes only, no free run)
osc main mute
# generate random notes with constant random and switched part and
# store to notes file lead.kbd
random |2(AC)r(DE)G|3(AC)c(DC). 9789 c-fgCDA.'',, crr-:S12 lead
# store piano sound with notes from file lead to memory 3
add piano lead 3
# store saxophone sound with notes from file lead to memory 0
add Saxophone lead 0
# play memory 3 with amplitude 60%
play 3 amp 60
# wait for 1 second
pause 1
# play memory 0 with amplitude 60%
play 0 amp 60
# wait for the return key being pressed
pause key

### 3rd party products
RtAudio library from github
ffmpeg in order to convert wav to mp3 files,
id3tool in order to add metadata to mp3 files
xterm terminal application
section is incomplete
### Installation
section is incomplete

# Glossary
Summary of sndlab specific technical terms
FMO	Frequency Modulating Oscillator / connected to Main
Hz	frequency unit / Oscillations per sec.
OSC, main	Main Oscillator that generates the audio out data.
max frequency	‪=55[Hz] * 2⁶ = 3520[Hz] => max octave is 5‬
max octave	max octave is 5‬, so that 55*2⁵*(1+1)=3520 (max_frequency)
min duration	1 sec / notes per second, see also note duration
Storage array (StA)	8 arrays of memory used to store sound data(0..5) can be user defined.
Note length, note duration	default 250 msec. the value can be change by the command: notes per_second #
note sentence / sentence length	some note words, see below. with / length: words * word length
Note specifiers	| , ' - . see table notes
Note values	see table notes
note word / word length	set of notes matching into a time slice of one second. / (word length = 1 second)
one second =	sample rate (AudioServer) / max frames (Synthesizer) 48000/48000
Oscillator, Osc	Waveform generating unit of the synthesizer (main, vco, fmo)
Program	main.synth and user defined include files
real time	The execution of a command needs to be committed by the synthesizer. The composer shows the time a commit needs for a composer command. If this time << 1000 ms we assume real time processing. / The conversion of sound into mp3 files is not real time
VCO	Volume Controlling Oscillator / connected to Main
Wave form	standard shapes of the time resolved amplitude (see table Standard Waveforms and wfid's)

### Planning features
2. Provide defaults for sub note sets like (c-Dur,
3. long notes. e.g B--- --c- = B--- B-c- no! impacts attack/decay
Execution text multi line: Exit with empty line